## Soil Moisture Sensor
## What is a Soil Moisture Sensor?
The soil moisture sensor is one kind of sensor used to gauge the volumetric content of water within the soil. As the straight gravimetric dimension of soil moisture needs eliminating, drying, as well as sample weighting. These sensors measure the volumetric water content not directly with the help of some other rules of soil like dielectric constant, electrical resistance, otherwise interaction with neutrons, and replacement of the moisture content.
The relation among the calculated property as well as moisture of soil should be adjusted & may change based on ecological factors like temperature, type of soil, otherwise electric conductivity. The microwave emission which is reflected can be influenced by the moisture of soil as well as mainly used in agriculture and remote sensing within hydrology.

### Working Principle
This sensor mainly utilizes capacitance to gauge the water content of the soil (dielectric permittivity). The working of this sensor can be done by inserting this sensor into the earth and the status of the water content in the soil can be reported in the form of a percent.
This sensor makes it perfect to execute experiments within science courses like environmental science, agricultural science, biology, soil science, botany, and horticulture.
### Specifications
The specification of this sensor includes the following.
- The required voltage for working is 5V
- The required current for working is <20mA
- Type of interface is analog
- The required working temperature of this sensor is 10°C~30°C
### Soil Moisture Sensor Applications
The applications of moisture sensor include the following.
- Agriculture
- Landscape irrigation
- Research
- Simple sensors for gardeners
This is all about the soil moisture sensor.